## Slide 1
Digital Logic Design and Application
Topic 1 - Introduction Yan Bo
School of Information & Communication Engineering, UESTC
Email: yanboyu@uestc.edu.cn

## Slide 2
QQ Group

## Slide 3: Topic1： Introduction
Why to do
What to do
How to do
Digital world
Info. for Course
Organization of CPU
Mathematic Foundations
EDA technology
Technology Related
Architecture of computer

## Slide 4: Topic1： Introduction
Why to do
What to do
How to do
Digital world
Info. for Course
Organization of CPU
Mathematic Foundations
EDA technology
Technology Related
Architecture of computer

## Slide 5: Topic1： Introduction
Why to do
What to do
How to do
Digital world
Info. for Course
Organization of CPU
Mathematic Foundations
EDA technology
Technology Related
Architecture of computer

## Slide 6: What are you thinking about ？
Digital circuit, Logic circuit
Digital system, Logic system

## Slide 7: What are you thinking about ？
Digital circuit, Logic circuit
Digital system, Logic system
Computer
Embedded Computer System
Embedded System

## Slide 8: What are you thinking about ？
Digital circuit, Logic circuit
Digital system, Logic system
Computer
Embedded Computer System
Embedded System
Smart Device
Unmanned…
Auto…
AI…

## Slide 9: The digital systems in a normal car

## Slide 10: The digital systems in a normal car

## Slide 11: The digital systems in a normal car
Windows

## Slide 12: The digital systems in a normal car
Windows
Door locks

## Slide 13: The digital systems in a normal car
Windows
Door locks
GPS

## Slide 14: The digital systems in a normal car
Windows
Door locks
Lights
GPS

## Slide 15: The digital systems in a normal car
Windows
Door locks
Lights
Anti-Brake
GPS

## Slide 16: The digital systems in a normal car
Windows
Door locks
Lights
Anti-Brake
Centre controller
GPS

## Slide 17: More digital systems in a self-driving car
Notes: ded ˈrekənɪŋ/ 航位推算
navigation system 导航系统

## Slide 18: Digital systems are everywhere
Notes: Exoskeleton robot
autonomous cart
unmanned vehicle
unmanned aerial vehicle (UAV)
unmanned drone
These objects all contain multiple computers inside.

## Slide 19: Digital systems are everywhere
Notes: Exoskeleton robot
autonomous cart
unmanned vehicle
unmanned aerial vehicle (UAV)
unmanned drone
These objects all contain multiple computers inside.

## Slide 20: Digital systems are everywhere
Notes: Exoskeleton robot
autonomous cart
unmanned vehicle
unmanned aerial vehicle (UAV)
unmanned drone
These objects all contain multiple computers inside.

## Slide 21: Digital systems are everywhere
Notes: Exoskeleton robot
autonomous cart
unmanned vehicle
unmanned aerial vehicle (UAV)
unmanned drone
These objects all contain multiple computers inside.

## Slide 22: Digital systems are everywhere
Notes: Exoskeleton robot
autonomous cart
unmanned vehicle
unmanned aerial vehicle (UAV)
unmanned drone
These objects all contain multiple computers inside.

## Slide 23: Digital systems are everywhere
Notes: Exoskeleton robot
autonomous cart
unmanned vehicle
unmanned aerial vehicle (UAV)
unmanned drone
These objects all contain multiple computers inside.

## Slide 24: Digital systems are everywhere
Notes: Exoskeleton robot
autonomous cart
unmanned vehicle
unmanned aerial vehicle (UAV)
unmanned drone
These objects all contain multiple computers inside.

## Slide 25: the computer world and the real world
2026-08-30
24

## Slide 26: the computer world and the real world
Real World
Computer World
2026-08-30
25

## Slide 27: the computer world and the real world
Real World
Computer World
2026-08-30
Digital
26

## Slide 28: the computer world and the real world
Real World
Computer World
2026-08-30
Digital
Analogue
27

## Slide 29: the computer world and the real world
Real World
Computer World
2026-08-30
28
Sound
Light
Smell
Temperature
Pressure
…….
Digital
Analogue

## Slide 30: the computer world and the real world
Real World
Computer World
2026-08-30
Sound
Light
Smell
Temperature
Pressure
…….
Digital
Analogue
Digital Signal
29

## Slide 31: the computer world and the real world
Real World
Computer World
2026-08-30
30
Sound
Light
Smell
Temperature
Pressure
…….
Digital
Analogue
Digital Signal

## Slide 32: the computer world and the real world
Real World
Computer World
2026-08-30
Sound
Light
Smell
Temperature
Pressure
…….
ADC(Sensors)
Digital
Analogue
Digital Signal
31

## Slide 33: the computer world and the real world
Real World
Computer World
2026-08-30
Sound
Light
Smell
Temperature
Pressure
…….
ADC(Sensors)
Digital
Analogue
Digital Signal
DAC(Actuator)
32

## Slide 34: the computer world and the real world
CPU
Real World
Computer World
2026-08-30
Sound
Light
Smell
Temperature
Pressure
…….
ADC(Sensors)
Digital
Analogue
Digital Signal
DAC(Actuator)
33

## Slide 35: the computer world and the real world
CPU
MEM
Real World
Computer World
2026-08-30
34
Sound
Light
Smell
Temperature
Pressure
…….
ADC(Sensors)
Digital
Analogue
Digital Signal
DAC(Actuator)

## Slide 36: the computer world and the real world
CPU
MEM
I/O
Real World
Computer World
2026-08-30
35
Sound
Light
Smell
Temperature
Pressure
…….
ADC(Sensors)
Digital
Analogue
Digital Signal
DAC(Actuator)

## Slide 37: the computer world and the real world
CPU
MEM
I/O
Real World
Computer World
2026-08-30
Sound
Light
Smell
Temperature
Pressure
…….
ADC(Sensors)
Digital
Analogue
Digital Signal
DAC(Actuator)
36
Notes: The most common actuator is a motor

## Slide 38: Topic1： Introduction
Why to do
What to do
How to do
Digital world
Info. for Course
Organization of CPU
Mathematic Foundations
EDA technology
Technology Related
Architecture of computer

## Slide 39: Development of Information Process

## Slide 40: Development of Information Process
Stone

## Slide 41: Development of Information Process
Stone
Abacus

## Slide 42: Development of Information Process
Stone
Abacus
Slide Rule

## Slide 43: Development of Information Process
Stone
Abacus
Slide Rule
1st Mechanical Calculator (1642)

## Slide 44: Development of Information Process
Stone
Abacus
Slide Rule
1st Mechanical Calculator (1642)
Improved Mechanical Calculator

## Slide 45: Development of the Electromagnetic Tech.

## Slide 46: Development of the Electromagnetic Tech.
Thunder

## Slide 47: Development of the Electromagnetic Tech.
Thunder
Compass

## Slide 48: Development of the Electromagnetic Tech.
Thunder
Compass
1st Morse telegraph(1837)

## Slide 49: Development of the Electromagnetic Tech.
Thunder
Compass
1st Morse telegraph(1837)
1st Bell telephone
(1876)

## Slide 50: Development of the Electromagnetic Tech.
Thunder
Compass
1st Morse telegraph(1837)
1st Bell telephone
(1876)
1st Light Bulb
(1880)

## Slide 51: Development of the Electromagnetic Tech.
Thunder
Compass
1st Morse telegraph(1837)
1st Bell telephone
(1876)
1st Light Bulb
(1880)
1st Vacuum
Diode (1904)
1st Vacuum
Triode (1907)

## Slide 52: Information Process Meet Electronic Tech.

## Slide 53: Information Process Meet Electronic Tech.

## Slide 54: Information Process Meet Electronic Tech.
Alan M. Turing
(1912-1954）
Father of
Artificial Intelligence

## Slide 55: Information Process Meet Electronic Tech.
Alan M. Turing
(1912-1954）
Father of
Artificial Intelligence
Turing Bombe（1940）

## Slide 56: Information Process Meet Electronic Tech.
Alan M. Turing
(1912-1954）
Father of
Artificial Intelligence
Turing Bombe（1940）
Vacuum tube (triode)

## Slide 57: Information Process Meet Electronic Tech.
Alan M. Turing
(1912-1954）
Father of
Artificial Intelligence
Turing Bombe（1940）
Vacuum tube (triode)

## Slide 58: Information Process Meet Electronic Tech.
Alan M. Turing
(1912-1954）
Father of
Artificial Intelligence
Turing Bombe（1940）
Claude E. Shannon
(1916-2001)
Father of
Information Theory
Vacuum tube (triode)

## Slide 59: Information Process Meet Electronic Tech.
Alan M. Turing
(1912-1954）
Father of
Artificial Intelligence
Turing Bombe（1940）
Claude E. Shannon
(1916-2001)
Father of
Information Theory
Theoretical basis of digital world
(1938)
Vacuum tube (triode)

## Slide 60: Information Process Meet Microelectronic Tech.

## Slide 61: Information Process Meet Microelectronic Tech.
Vacuum tube (triode)

## Slide 62: Information Process Meet Microelectronic Tech.
Vacuum tube (triode)
1st Integrated Circuit
By TI Corporation
（1958）
Solid-state circuit

## Slide 63: Information Process Meet Microelectronic Tech.
Vacuum tube (triode)
1st Transistor
by Bell Laboratory (1947)
1st Integrated Circuit
By TI Corporation
（1958）
Solid-state circuit

## Slide 64: Information Process Meet Microelectronic Tech.
Vacuum tube (triode)
1st Transistor
by Bell Laboratory (1947)
1st Integrated Circuit
By TI Corporation
（1958）
Solid-state circuit
1st planar Integrated Circuit
by Fairchild Semiconductor （1960）

## Slide 65: Information Process Meet Microelectronic Tech.
Vacuum tube (triode)
1st Transistor
by Bell Laboratory (1947)
1st Integrated Circuit
By TI Corporation
（1958）
Solid-state circuit
1st planar Integrated Circuit
by Fairchild Semiconductor （1960）
Modern CPU chip

## Slide 66: Development of Semiconductor Tech.
65

## Slide 67: Development of Semiconductor Tech.
Transistors per Integrated Circuit doubles every 18 months.
---Gooden Moore, 1965
66

## Slide 68: Development of Semiconductor Tech.
4004（1971）
2300 transistors
Pentium 4 Xeon （2000）
42 million transistors
Xeon（2008）
1900 million transistors
Transistors per Integrated Circuit doubles every 18 months.
---Gooden Moore, 1965
67

## Slide 69: More Than Moore & Beyond Moore

## Slide 70: More Than Moore & Beyond Moore
More Moore: Scaling as per Moore’s law.

## Slide 71: More Than Moore & Beyond Moore
More Moore: Scaling as per Moore’s law.
More than Moore: Functional Diversification, Application driven components

## Slide 72: More Than Moore & Beyond Moore
More Moore: Scaling as per Moore’s law.
More than Moore: Functional Diversification, Application driven components
Beyond Moore: Beyond CMOS

## Slide 73: Topic1： Introduction
Why to do
What to do
How to do
Digital world
Info. for Course
Organization of CPU
Mathematic Foundations
EDA technology
Technology Related
Architecture of computer

## Slide 74: Topic1： Introduction
Why to do
What to do
How to do
Digital world
Info. for Course
Organization of CPU
Mathematic Foundations
EDA technology
Technology Related
Architecture of computer

## Slide 75: The overall plan of the whole course
Central Process Unit
Datapath
(ALU, MUX…)
Controller
(State Machine)
TEST
Boolean Algebra
Gates
Combinational Circuit
Sequential
Circuit
Notes: This is the big picture for the whole course
This is the overall plan of the whole course

## Slide 76: The overall plan of the whole course
Central Process Unit
Datapath
(ALU, MUX…)
Controller
(State Machine)
TEST
Boolean Algebra
Gates
Combinational Circuit
Sequential
Circuit
1.Notation of number, base conversion
2. Laws of Boolean algebra
1.Basic gates
2.Mninal complete set
3.Analogy feature:noise margin,fan in/out
Notes: We’ll start with Boolean algebra and basic gates

## Slide 77: The overall plan of the whole course
Central Process Unit
Datapath
(ALU, MUX…)
Controller
(State Machine)
TEST
Boolean Algebra
Gates
Combinational Circuit
Sequential
Circuit
1.Notation of number, base conversion
2. Laws of Boolean algebra
Truth table, K-map, logic expression
Design for Combinational circuit
  Gates
  On-shelf chip: Decoder, MUX
  HDL & EDA
Analysis for Combination Circuit
Analogy feature: hazard
STG, State transition/Output table
Design for Sequential Circuit
  F/F＋Combinational circuit
  On-shelf chips: shift register, counter
  HDL & EDA
Analysis for Sequetial Circuit
Analogy feature：
key path，setup time, hold time
1.Basic gates
2.Mninal complete set
3.Analogy feature:noise margin,fan in/out
Notes: Then we’ll discuss how to analysis and design the simple combinational circuit modules and sequential circuit modules

## Slide 78: The overall plan of the whole course
Central Process Unit
Datapath
(ALU, MUX…)
Controller
(State Machine)
TEST
Boolean Algebra
Gates
Combinational Circuit
Sequential
Circuit
1.Notation of number, base conversion
2. Laws of Boolean algebra
Truth table, K-map, logic expression
Design for Combinational circuit
  Gates
  On-shelf chip: Decoder, MUX
  HDL & EDA
Analysis for Combination Circuit
Analogy feature: hazard
STG, State transition/Output table
Design for Sequential Circuit
  F/F＋Combinational circuit
  On-shelf chips: shift register, counter
  HDL & EDA
Analysis for Sequetial Circuit
Analogy feature：
key path，setup time, hold time
Specification： define ISA
Top-design：
  Port
  Datapath＋Controller＋Interconnect
Submodule-design according to ISA
Testbench, performance assessment
1.Basic gates
2.Mninal complete set
3.Analogy feature:noise margin,fan in/out

## Slide 79: From Boolean Algebra to CPU
1.数的表示法，不同进制之间的转换；
2.布尔代数的公理、常用定理；
基本描述方法：真值表，K图，逻辑式
组合电路设计方法
  用门电路实现
  用已有模块搭建：级联，译码器，复用器
  HDL语言描述，综合
组合电路分析方法
电路模拟特性：竞争冒险
基本描述方法：STG, 状态转移/输出表
时序电路设计方法
  用DFF＋组合电路实现
  用已有模块搭建：移位寄存器，计数器
  HDL语言描述，综合
时序电路分析方法
电路模拟特性：关键路径, 建立/保持时间
规格定义： 指令集ISA
顶层设计：
  Port，
  Datapath＋Controller＋Interconnect
子模块设计：根据ISA分别设计
设计验证：testbench设计，性能评估
1.基本门；
2.最小完全集：电路形式的变换；
3.门的模拟特性：噪声容限，扇入，扇出
Central Process Unit
Datapath
(ALU, MUX…)
Controller
(State Machine)
TEST
Boolean Algebra
Gates
Combinational Circuit
Sequential
Circuit

## Slide 80: Organization of Center Processor Unit
2026-08-30
Data Inputs
Data Outputs
Controller
Datapath
Control Signals
Status Signals
Control Inputs
(Instruction)
Control Outputs

## Slide 81: Schedule for Teaching & Learning
Every lecture and lab is last for 3 hours
Team up as you want: 5 persons/team
Totally we have 6 presentations
For every team & every presentation
  10min. for presentation
  10min. for discussion
Grading
  Homework (Set Exercise) 5%
  Project 20%
  Output 10%
  Presentation 5%
  Report 5%
  Final Exam (Written Exam) 75%

## Slide 82: Schedule for Teaching & Learning
Every lecture and lab is last for 3 hours
Team up as you want: 3-5 persons/team
Totally we have 5 presentations
For every team & every presentation
  10min. for presentation
  10min. for discussion
Grading
  Homework (Set Exercise) 5%
  Project 20%
  Output 10%
  Presentation 5%
  Report 5%
  Final Exam (Written Exam) 75%

## Slide 83: Schedule for Teaching & Learning
 | Main Task | 19:00~ 22:00
Lecture 01 |  | 
Lecture 02 | Design of Dataflow (Team Presentation & Discussion) | 
Lecture 03 | Design of Datapath & Controller (Team Presentation & Discussion) | 
Lecture 04 | Verification of Datapath & Controller (Team Presentation & Discussion) | 
Lecture05 |  | 
Lecture 06 | Integration & Verification of RISC CPU (Team Presentation & Discussion) | 
Lecture 07 |  | 
Lecture 08 |  | 
Lecture 09 |  | 
Lecture 10 | RoadShow (Team Presentation & Discussion) | 
Lecture 11 |  | 
Every lecture and lab is last for 3 hours
Team up as you want: 5 persons/team
Totally we have 5 presentations
For every team & every presentation
  10min. for presentation
  10min. for discussion
Grading
  Homework (Set Exercise) 5%
  Project 20%
  Output 10%
  Presentation 5%
  Report 5%
  Final Exam (Written Exam) 75%

## Slide 84: Schedule for Teaching & Learning
 | Main Task | 19:00~ 22:00
Lecture 01 |  | 
Lecture 02 | Design of Dataflow (Team Presentation & Discussion) | 
Lecture 03 | Design of Datapath & Controller (Team Presentation & Discussion) | 
Lecture 04 | Verification of Datapath & Controller (Team Presentation & Discussion) | 
Lecture05 |  | 
Lecture 06 | Integration & Verification of RISC CPU (Team Presentation & Discussion) | 
Lecture 07 |  | Lab1
Lecture 08 |  | Lab2
Lecture 09 |  | Lab3
Lecture 10 | RoadShow (Team Presentation & Discussion) | Lab4
Lecture 11 |  | Lab5
Every lecture and lab is last for 3 hours
Team up as you want: 5 persons/team
Totally we have 5 presentations
For every team & every presentation
  10min. for presentation
  10min. for discussion
Grading
  Homework (Set Exercise) 5%
  Project 20%
  Output 10%
  Presentation 5%
  Report 5%
  Final Exam (Written Exam) 75%

## Slide 85: Schedule for Teaching & Learning
 | Main Task | 19:00~ 22:00
Lecture 01 | Introduction | 
Lecture 02 | Design of Dataflow (Team Presentation & Discussion) | 
Lecture 03 | Design of Datapath & Controller (Team Presentation & Discussion) | 
Lecture 04 | Verification of Datapath & Controller (Team Presentation & Discussion) | 
Lecture05 |  | 
Lecture 06 | Integration & Verification of RISC CPU (Team Presentation & Discussion) | 
Lecture 07 |  | Lab1
Lecture 08 |  | Lab2
Lecture 09 |  | Lab3
Lecture 10 | RoadShow (Team Presentation & Discussion) | Lab4
Lecture 11 |  | Lab5
Every lecture and lab is last for 3 hours
Team up as you want: 5 persons/team
Totally we have 5 presentations
For every team & every presentation
  10min. for presentation
  10min. for discussion
Grading
  Homework (Set Exercise) 5%
  Project 20%
  Output 10%
  Presentation 5%
  Report 5%
  Final Exam (Written Exam) 75%

## Slide 86: Schedule for Teaching & Learning
 | Main Task | 19:00~ 22:00
Lecture 01 | Introduction | 
Lecture 02 | Design of Dataflow (Team Presentation & Discussion) | 
Lecture 03 | Design of Datapath & Controller (Team Presentation & Discussion) | 
Lecture 04 | Verification of Datapath & Controller (Team Presentation & Discussion) | 
Lecture05 | Design & Document | 
Lecture 06 | Integration & Verification of RISC CPU (Team Presentation & Discussion) | 
Lecture 07 |  | Lab1
Lecture 08 |  | Lab2
Lecture 09 |  | Lab3
Lecture 10 | RoadShow (Team Presentation & Discussion) | Lab4
Lecture 11 |  | Lab5
Every lecture and lab is last for 3 hours
Team up as you want: 5 persons/team
Totally we have 5 presentations
For every team & every presentation
  10min. for presentation
  10min. for discussion
Grading
  Homework (Set Exercise) 5%
  Project 20%
  Output 10%
  Presentation 5%
  Report 5%
  Final Exam (Written Exam) 75%

## Slide 87: Schedule for Teaching & Learning
 | Main Task | 19:00~ 22:00
Lecture 01 | Introduction | 
Lecture 02 | Design of Dataflow (Team Presentation & Discussion) | 
Lecture 03 | Design of Datapath & Controller (Team Presentation & Discussion) | 
Lecture 04 | Verification of Datapath & Controller (Team Presentation & Discussion) | 
Lecture05 | Design & Document | 
Lecture 06 | Integration & Verification of RISC CPU (Team Presentation & Discussion) | 
Lecture 07 | Others about the Combinational Circuit | Lab1
Lecture 08 | Others about the Combinational Circuit | Lab2
Lecture 09 | Others about the Sequential Circuit | Lab3
Lecture 10 | RoadShow (Team Presentation & Discussion) | Lab4
Lecture 11 |  | Lab5
Every lecture and lab is last for 3 hours
Team up as you want: 5 persons/team
Totally we have 5 presentations
For every team & every presentation
  10min. for presentation
  10min. for discussion
Grading
  Homework (Set Exercise) 5%
  Project 20%
  Output 10%
  Presentation 5%
  Report 5%
  Final Exam (Written Exam) 75%

## Slide 88: Schedule for Teaching & Learning
 | Main Task | 19:00~ 22:00
Lecture 01 | Introduction | 
Lecture 02 | Design of Dataflow (Team Presentation & Discussion) | 
Lecture 03 | Design of Datapath & Controller (Team Presentation & Discussion) | 
Lecture 04 | Verification of Datapath & Controller (Team Presentation & Discussion) | 
Lecture05 | Design & Document | 
Lecture 06 | Integration & Verification of RISC CPU (Team Presentation & Discussion) | 
Lecture 07 | Others about the Combinational Circuit | Lab1
Lecture 08 | Others about the Combinational Circuit | Lab2
Lecture 09 | Others about the Sequential Circuit | Lab3
Lecture 10 | RoadShow (Team Presentation & Discussion) | Lab4
Lecture 11 | Course Review | Lab5
Every lecture and lab is last for 3 hours
Team up as you want: 5 persons/team
Totally we have 5 presentations
For every team & every presentation
  10min. for presentation
  10min. for discussion
Grading
  Homework (Set Exercise) 5%
  Project 20%
  Output 10%
  Presentation 5%
  Report 5%
  Final Exam (Written Exam) 75%

## Slide 89: Schedule for Teaching & Learning
 | Main Task | 19:00~ 22:00
Lecture 01 | Introduction | 
Lecture 02 | Design of Dataflow (Team Presentation & Discussion) | 
Lecture 03 | Design of Datapath & Controller (Team Presentation & Discussion) | 
Lecture 04 | Verification of Datapath & Controller (Team Presentation & Discussion) | 
Lecture05 | Design & Document | 
Lecture 06 | Integration & Verification of RISC CPU (Team Presentation & Discussion) | 
Lecture 07 | Others about the Combinational Circuit DDL for Homework 1+2: 11/10/2026, WEEK7 | Lab1
Lecture 08 | Others about the Combinational Circuit | Lab2
Lecture 09 | Others about the Sequential Circuit | Lab3
Lecture 10 | RoadShow (Team Presentation & Discussion) | Lab4
Lecture 11 | Course Review DDL for Homework 3+4+5: 15/11/2026, WEEK12 | Lab5
Every lecture and lab is last for 3 hours
Team up as you want: 5 persons/team
Totally we have 5 presentations
For every team & every presentation
  10min. for presentation
  10min. for discussion
Grading
  Homework (Set Exercise) 5%
  Project 20%
  Output 10%
  Presentation 5%
  Report 5%
  Final Exam (Written Exam) 75%

## Slide 90: Schedule for Teaching & Learning
 | Main Task | 19:00~ 22:00
Lecture 01 | Introduction | 
Lecture 02 | Design of Dataflow (Team Presentation & Discussion) | 
Lecture 03 | Design of Datapath & Controller (Team Presentation & Discussion) | 
Lecture 04 | Verification of Datapath & Controller (Team Presentation & Discussion) | 
Lecture05 | Design & Document | 
Lecture 06 | Integration & Verification of RISC CPU (Team Presentation & Discussion) | 
Lecture 07 | Others about the Combinational Circuit DDL for Homework 1+2: 11/10/2026, WEEK7 | Lab1
Lecture 08 | Others about the Combinational Circuit | Lab2
Lecture 09 | Others about the Sequential Circuit | Lab3
Lecture 10 | RoadShow (Team Presentation & Discussion) DDL for Report: 13/12/2026, WEEK16 | Lab4
Lecture 11 | Course Review DDL for Homework 3+4+5: 15/11/2026, WEEK12 | Lab5
Every lecture and lab is last for 3 hours
Team up as you want: 5 persons/team
Totally we have 5 presentations
For every team & every presentation
  10min. for presentation
  10min. for discussion
Grading
  Homework (Set Exercise) 5%
  Project 20%
  Output 10%
  Presentation 5%
  Report 5%
  Final Exam (Written Exam) 75%

## Slide 91: For Project(Pres. & Disc.) 20%
Basic Instruction Set for RISC CPU |  |  |  |  | 
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1

## Slide 92: For Project(Pres. & Disc.) 20%
16-bit RISC CPU with:
at most 16 instructions (4-bit for Opcode )
at most 4 registers (2-bit for Rd and Rs)
Basic Instruction Set for RISC CPU |  |  |  |  | 
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1

## Slide 93: For Project(Pres. & Disc.) 20%
Technical level (team) |  |  | 
C_Level(only support basic instructions): 6’ |  |  | 
16-bit RISC CPU with:
at most 16 instructions (4-bit for Opcode )
at most 4 registers (2-bit for Rd and Rs)
Basic Instruction Set for RISC CPU |  |  |  |  | 
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1

## Slide 94: For Project(Pres. & Disc.) 20%
Technical level (team) |  |  | 
B_Level(can run on a real FPGA): 7’ C_Level(only support basic instructions): 6’ |  |  | 
16-bit RISC CPU with:
at most 16 instructions (4-bit for Opcode )
at most 4 registers (2-bit for Rd and Rs)
Basic Instruction Set for RISC CPU |  |  |  |  | 
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1

## Slide 95: For Project(Pres. & Disc.) 20%
Technical level (team) |  |  | 
A_Level(can support more instructions): 8’ B_Level(can run on a real FPGA): 7’ C_Level(only support basic instructions): 6’ |  |  | 
16-bit RISC CPU with:
at most 16 instructions (4-bit for Opcode )
at most 4 registers (2-bit for Rd and Rs)
Basic Instruction Set for RISC CPU |  |  |  |  | 
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1

## Slide 96: For Project(Pres. & Disc.) 20%
Technical level (team) |  |  | 
A_Level(can support more instructions): 8’ B_Level(can run on a real FPGA): 7’ C_Level(only support basic instructions): 6’ |  |  | 
16-bit RISC CPU with:
at most 16 instructions (4-bit for Opcode )
at most 4 registers (2-bit for Rd and Rs)
Basic Instruction Set for RISC CPU |  |  |  |  | 
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1
Some idea for enlarging the basic Instruction Set:
Memory access instructions
ldr, str
Conditional branch instructions
jz, jnc, …
Other data operation instructions
  xor, cmp, acc (add 1 to N)

## Slide 97: For Project(Pres. & Disc.) 20%
Technical level (team) |  |  | Workload (individual)
A_Level(can support more instructions): 8’ B_Level(can run on a real FPGA): 7’ C_Level(only support basic instructions): 6’ |  |  | Distributed by yourself Average 2’ for each people Up to 4’ for each, no negative marks
16-bit RISC CPU with:
at most 16 instructions (4-bit for Opcode )
at most 4 registers (2-bit for Rd and Rs)
Basic Instruction Set for RISC CPU |  |  |  |  | 
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1
Some idea for enlarging the basic Instruction Set:
Memory access instructions
ldr, str
Conditional branch instructions
jz, jnc, …
Other data operation instructions
  xor, cmp, acc (add 1 to N)

## Slide 98: For Project(Pres. & Disc.) 20%
Technical level (team) |  | Pres. & Disc. (individual) | Workload (individual)
A_Level(can support more instructions): 8’ B_Level(can run on a real FPGA): 7’ C_Level(only support basic instructions): 6’ |  | +0~5’ Clearly | Distributed by yourself Average 2’ for each people Up to 4’ for each, no negative marks
16-bit RISC CPU with:
at most 16 instructions (4-bit for Opcode )
at most 4 registers (2-bit for Rd and Rs)
Basic Instruction Set for RISC CPU |  |  |  |  | 
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1
Some idea for enlarging the basic Instruction Set:
Memory access instructions
ldr, str
Conditional branch instructions
jz, jnc, …
Other data operation instructions
  xor, cmp, acc (add 1 to N)

## Slide 99: For Project(Pres. & Disc.) 20%
Technical level (team) | Document (team) | Pres. & Disc. (individual) | Workload (individual)
A_Level(can support more instructions): 8’ B_Level(can run on a real FPGA): 7’ C_Level(only support basic instructions): 6’ | +0~5’ Completely | +0~5’ Clearly | Distributed by yourself Average 2’ for each people Up to 4’ for each, no negative marks
16-bit RISC CPU with:
at most 16 instructions (4-bit for Opcode )
at most 4 registers (2-bit for Rd and Rs)
Basic Instruction Set for RISC CPU |  |  |  |  | 
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1
Some idea for enlarging the basic Instruction Set:
Memory access instructions
ldr, str
Conditional branch instructions
jz, jnc, …
Other data operation instructions
  xor, cmp, acc (add 1 to N)

## Slide 100: Project assessment (20 marks in total)
Part1: Team assessment Technical level 6~8’+ Document 0~5’
Part2: Individual assessment Pres.&Dissc. 0~5’+ Workload 0~4’
Class A(8~13’): Support more instruction and simulation signals could be explained.
Class B(7~12’): The design can run on a real FPGA board (e.g. as a LED Controller), and the internal signals could be observed through ILA IP core.
Class C(6~11’): Support basic instructions and simulation signals could be explained.
** Code can be simulated and synthesized directly.
** Codes and reports will be checked for duplicates.
** The marks is better if pipeline or instruction accelerator could be added to Class A
Pres.&Dissc (0~5’): Assess separately for each student
Workload(0~4’): Distributed by yourself.
Average 2’ for each people; up to 4’ for each one; no negative marks.

## Slide 101
Task description: Class C (6`)
1. Familiar with EDA software
2. Complete the structure design (Datapath + Controller) according to the basic instruction set
3. Compose Verilog code for design and do synthesis
4. Compose Verilog code for testbench and do simulation
Instruction Format
Basic Instruction Set
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1

## Slide 102
1. Design a application demo (LED controller, etc.) base on your CPU chip
2. Download the bitstream to a real FPGA board
3. Use ILA IP core to do debug
Task description: Class B (7`)

## Slide 103
1. Add more instruction (load/ store, etc.) to basic instruction set.
2. Modify hardware structure and design code to implementing new instruction set.
3. Modify testbench code, do simulation and implement on a FPGA.
Add memory or I/O ports to testbench
Task description: Class A (8`)

## Slide 104: 项目实践一共20分，包括两个部分：
Part1: 团队分 实现难度6~8’ + 设计文档0~5’
Part2: 个人分 报告讨论0~5’ + 组内工作0~4’
A档(8~13分)：支持更多指令（如load/store），并完成仿真测试
B档(7~12分)：能够下板运行（如控制流水灯），会用ILA进行指令抓取
C档(6~11分)： 支持基本指令集，并完成仿真测试
PS：代码必须能直接仿真综合否则视为无效；
代码与报告均会查重；
在A档基础上做下流水线或指令加速器，可进一步提高分数
平时研讨(0~5分)：每个同学分别打分
组内工作(0~4分)：由组内自行讨论分配
平均每人2’, 每人分数最高不超过4’，没有负分

## Slide 105
C档任务说明
6’
1. 熟练使用EDA软件
2. 根据基础指令集完成硬件结构 设计： 数据通路+控制通路
3. 编写Verilog代码，并完成综合
4. 编写TestBench ，并完成仿真验证
指令格式
基本指令集
Opcode 4bit | Rd 2bit | Rs 2bit | Imme 8bit | Assembly | Function Description
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | mov r1 #02 mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | add r1 #08 add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | and R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | jump #01 | PC<= 1

## Slide 106
1. 设计好的CPU电路下板测试
2. 使用ILA抓取信号，验证功能的正确性
3. 加入流水灯控制，完成应用演示
B档任务说明
7’

## Slide 107
在基础指令集基础上：
1. 增加新指令，如load/ store
2. 修改硬件架构及Verilog代码
3. 编写TestBench，并完成仿真验证
4. 完成下板测试及应用演示
TestBench考虑添加内存或I/O端口
A档任务说明
8’

## Slide 108
Vivado Project
Testbench Code example
Files for Project

## Slide 109
Files for Project

## Slide 110
2026-08-30
109

## Slide 111: 参考材料的使用
3. For_IC_Newer
Vivado软件及Verilog语言入门
1.Lab_Refrence（先浏览一遍，琢磨下跟项目任务的关系）
CPU设计实验课件（普通班）
2. Design_Doc_Template（设计文档模板）
大框架不变，小节可自行补充或删减

## Slide 112: 项目文档(doc+ppt)编写说明
第一次研讨课需分组用ppt汇报的部分
设计文档和演示文档统一命名为“班号组号_日期”，如：12_20240214
设计文档（doc）只有一个，大家在学习过程中不断补充和完善其内容即可；
演示文档（ppt）每次研讨时都应重新做，把本次上课需要讲的内容（主要是图、表）从doc文件中取出来做成ppt。当然，ppt文件也应该是个相对独立和完整的文件，有些内容（比如系统大框图）可能每次ppt文件都需要，保留下来就行。
2026-08-30

## Slide 113: Requirements
2026-08-30
Textbook
“Digital System Design with Verilog & VHDL”
2nd Edition，Enoch O.Hwang著，阎波 朱晓章 姚毅改编
Publishing House of Electronics Industry，2018
Reference books
  “Digital Design: Principles and Practices"
4th Edition, John F. Wakerly，
  “数字逻辑设计及应用”,姜书艳等，电子科大出版社，2014
  “微处理器系统结构与嵌入式系统设计”
  第三版，阎波，李广军等，电子工业出版社，2020
  “数字集成电路与系统设计”
  李广军 郭志勇等，电子工业出版社，2015
  MOOC
  https://www.icourse163.org/learn/UESTC1-1458202164 （英文版数电）https://www.icourse163.org/course/UESTC-234014 （中文版数电）
  https://www.icourse163.org/course/UESTC-234015 （中文版ASIC设计）
112

## Slide 114: Office hours
2026-08-30
Office Hour
Monday 13：00-14：00
Office Address
  KB 224
  Email
  yanboyu@uestc.edu.cn (阎波)
113

## Slide 115: Topic1： Introduction
Why to do
What to do
How to do
Digital world
Info. for Course
Organization of CPU
Mathematic Foundations
EDA technology
Technology Related
Architecture of computer

## Slide 116: Architecture of Von Neumann computer
2026-08-30
115

## Slide 117: Architecture of Von Neumann computer
Computer：
2026-08-30
116

## Slide 118: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
2026-08-30
117

## Slide 119: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
2026-08-30
118

## Slide 120: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
2026-08-30
119

## Slide 121: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
Input
Output
2026-08-30
120

## Slide 122: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
Input
Output
2026-08-30
121

## Slide 123: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
Input
Output
2026-08-30
122

## Slide 124: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
Input
Output
2026-08-30
123

## Slide 125: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
Input
Output
CPU：
2026-08-30
124

## Slide 126: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
Input
Output
CPU：
2026-08-30
125

## Slide 127: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
Input
Output
CPU：
2026-08-30
126

## Slide 128: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
Input
Output
CPU：
2026-08-30
127

## Slide 129: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
Input
Output
CPU：
2026-08-30
Datapath
128

## Slide 130: Architecture of Von Neumann computer
Computer：
Operator
(ALU)
Controller
Memory
Input
Output
CPU：
Controller
Datapath
2026-08-30
Datapath
129

## Slide 131: Topic1： Introduction
Why to do
What to do
How to do
Digital world
Info. for Course
Organization of CPU
Technology Related
Architecture of computer
Mathematic Foundations
EDA technology

## Slide 132: Organization of Center Processor Unit
2026-08-30
Controller
Datapath
131

## Slide 133: Organization of Center Processor Unit
2026-08-30
Controller
Datapath
132

## Slide 134: Organization of Center Processor Unit
2026-08-30
Controller
Datapath
133

## Slide 135: Organization of Center Processor Unit
2026-08-30
Data Inputs
Data Outputs
Controller
Datapath
134

## Slide 136: Organization of Center Processor Unit
2026-08-30
Data Inputs
Data Outputs
Controller
Datapath
135

## Slide 137: Organization of Center Processor Unit
2026-08-30
Data Inputs
Data Outputs
Controller
Datapath
Control Signals
136

## Slide 138: Organization of Center Processor Unit
2026-08-30
Data Inputs
Data Outputs
Controller
Datapath
Control Signals
Status Signals
137

## Slide 139: Organization of Center Processor Unit
2026-08-30
138
Data Inputs
Data Outputs
Datapath
Control Signals
Status Signals
Control Inputs
(Instruction)
Control Outputs
Controller

## Slide 140: Organization of Center Processor Unit
2026-08-30
Data Inputs
Data Outputs
Controller
Datapath
Control Signals
Status Signals
Control Inputs
(Instruction)
Control Outputs
P1
139

## Slide 141
Fetch, Decoder, Execute
AB
DB
ALU
Register1(R1)
Temp Reg
Flag Register (FR)
Register File
(RF)
Operator Controller (OC)
Instruction Decoder (ID)
Instruction Register (IR)
Opcode, Operand
Internal BUS
Address Buffer
Data Buffer
Program Couter (PC)
Address Decoder
Read
B0
5C
04
2E
Address
1001
1002
1003
Data
1000
Internal Memory
Assembly language program
……
MOV 0x5C, R1
ADD R1, 0x2E, R1
……
＋1
Outside of CPU
Inside of CPU
①
②
③
④
⑤
⑥
①
②
③
④
⑤
⑥
①
③
④
⑤
⑥
②
①
②
③
④
⑤
⑥
⑦
⑧
Program Execution Process
2026-08-30
140
Notes: Principle of CPU

## Slide 142: Topic1： Introduction
Why to do
What to do
How to do
Digital world
Info. for Course
Organization of CPU
HDL Language
EDA technology
Technology Related
Architecture of computer

## Slide 143: Topic1： Introduction
Why to do
What to do
How to do
Digital world
Info. for Course
Organization of CPU
HDL Language
EDA technology
Technology Related
Architecture of computer

## Slide 144: VHDL vs. Verilog
Government Developed in 1981 | Commercially Developed in 1985
Ada based | C based
Strongly Type Cast | Mildly Type Cast
Case-insensitive | Case-sensitive
Difficult to learn | Easier to Learn
  VHDL is an acronym for :
  VHSIC (Very High Speed Integrated Circuit) Hardware Description Language
HDLs is used to describe a HARDWARE!
They are quite different with the tradition program language!
Chap1.4

## Slide 145: TOP-DOWN Design
Control Module
Datapath Module
PART 1
(combination)
PART 2
(combination)
PART 3
(sequential
FSM)
PART 1
(combination)
PART 2
(combination)
PART 4
(Register)
PART 3
(combination)
PART 5
(Counter)
Digital circuit
Top-level module
port-function
Interconnect
PART 4
(sequential
FSM)
Interconnect
Interconnect
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function

## Slide 146: Basic Verilog Modeling
module is a most basic building block of a design.
port_mode port_name1;
port_mode port_name2;
…………
circuit functionality describes an implementation of the corresponding module.
port declarations describes the interface of the component, i.e. input and output ports.
assign statements;
always @(sensitive signals list)
begin
functionality code
end
module module_name (port_name1,_port_name2, …);
port declarations
circuit functionality
endmodule
Interconnect declarations
wire interconnect_name1;
wire interconnect_name1;
…………

## Slide 147: Fundamental rules of Verilog
module MultiplexerC (w，a, b, s);
output reg w;
input a，b，s;
wire m;
assign m = a+b;
always @(a, b, s)
begin
if (s) w = b;
else w = m;
end
endmodule
module name
reserved words
lowercase
Semicolon
No Semicolon
Continuous Assignment statement is used if the unit is simple
Procedural Block(always)
statement with sensitivity list is used when the unit is too complex
Declare port and inter-connect signal
module ports
The signal assigned in always block should be ‘reg’ type

## Slide 148: Verilog Design Styles
Components and
interconnects
structural
behavioral
(sequential)
Subset most suitable for synthesis
Testbenches
I1
I2
Y
I1
I2
Y
U1_OUT
module structural (Result, A, B, C);
output Result;
input A, B, C;
wire U1_OUT;
xor U1(U1_OUT,A,B); xor U2(Result,U1_OUT,C);
endmodule
module behavioral (Result, A, B, C);
output reg Result;
input A, B, C;
always @ (A, B, C)
begin
Result = (A ^ B) ^ C;
end
endmodule
dataflow
Concurrent statements
module dataflow (Result, A, B, C);
output Result;
input A, B, C;
assign Result = (A ^ B) ^ C;
endmodule
Chap1.2

## Slide 149: Octal 2-to-1 MUX
condition ？true_expression：false_expression
module Mux8 (
);
endmodule
output[7:0] bus1,
input sel,
input [7:0] data1, data0
assign ;
bus1 = sel ? data1 : data0
0
1
bus1
data1
data0
sel
8
8
8

## Slide 150: 3-to-1 MUX
HARDWARE!
a
sel
2
b
c
q
module Mux31a ( q, a , b, c, sel ) ;
endmodule
output q;
input a, b, c;
input [ 1:0 ] sel;
always @ ( * )
begin
end
case ( sel )
endcase
0: q = a ;
1: q = b;
2: q = c;
default: q = a;
module Mux31b ( q, a , b, c, sel ) ;
endmodule
output q;
input a, b, c;
input [ 1:0 ] sel;
always @ ( * )
begin
end
a
c
sel[1]
b
sel[0]
q
0
1
0
1
No priority
Priority!
if ( sel[0] == 1 ) q = b;
else if ( sel[1] == 1 ) q = c;
else q = a;
reg q;
reg q;
Assigned in Procedural Block
Default alternative
Else alternative
Assigned in Procedural Block

## Slide 151: Topic1： Introduction
Why to do
What to do
How to do
Digital system
Architecture of computer
Organization of CPU
HDL Language
EDA Design Flow
Info. for Course
Technology Related

## Slide 152: IC design methodology & EDA flow
Chap1.4~1.6

## Slide 153: IC design methodology & EDA flow
Design specification
Chap1.4~1.6

## Slide 154: IC design methodology & EDA flow
Design specification
Design partition
Chap1.4~1.6

## Slide 155: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Chap1.4~1.6

## Slide 156: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Chap1.4~1.6

## Slide 157: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Chap1.4~1.6

## Slide 158: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Chap1.4~1.6

## Slide 159: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Postsynthesis
functional verification
Postsynthesis
timing verification
Chap1.4~1.6

## Slide 160: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Postsynthesis
functional verification
Postsynthesis
timing verification
Test generation and
Fault simulation
Chap1.4~1.6

## Slide 161: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Postsynthesis
functional verification
Postsynthesis
timing verification
Test generation and
Fault simulation
Cell placement, scan chain and
clock tree insertion ,cell routing
Chap1.4~1.6

## Slide 162: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Postsynthesis
functional verification
Postsynthesis
timing verification
Test generation and
Fault simulation
Cell placement, scan chain and
clock tree insertion ,cell routing
Verify physical and Electrical design rules
Chap1.4~1.6

## Slide 163: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Postsynthesis
functional verification
Postsynthesis
timing verification
Test generation and
Fault simulation
Cell placement, scan chain and
clock tree insertion ,cell routing
Verify physical and Electrical design rules
Extract parasitic
Chap1.4~1.6

## Slide 164: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Postsynthesis
functional verification
Postsynthesis
timing verification
Test generation and
Fault simulation
Cell placement, scan chain and
clock tree insertion ,cell routing
Verify physical and Electrical design rules
Extract parasitic
Design sign-off
Chap1.4~1.6

## Slide 165: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Postsynthesis
functional verification
Postsynthesis
timing verification
Test generation and
Fault simulation
Cell placement, scan chain and
clock tree insertion ,cell routing
Verify physical and Electrical design rules
Extract parasitic
Design sign-off
Production-ready masks
Chap1.4~1.6

## Slide 166: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Postsynthesis
functional verification
Postsynthesis
timing verification
Test generation and
Fault simulation
Cell placement, scan chain and
clock tree insertion ,cell routing
Verify physical and Electrical design rules
Extract parasitic
Design sign-off
Production-ready masks
Chap1.4~1.6
Front-End
Back-End

## Slide 167: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Postsynthesis
functional verification
Postsynthesis
timing verification
Test generation and
Fault simulation
Cell placement, scan chain and
clock tree insertion ,cell routing
Verify physical and Electrical design rules
Extract parasitic
Design sign-off
Production-ready masks
Chap1.4~1.6
Front-End
Back-End
FPGA

## Slide 168: IC design methodology & EDA flow
Design specification
Design partition
Design entry: HDL
Behavioral modeling
Functional Verification
Design integration and
functional verification
Synthesize (implement)
and map Gate-level netlist
Postsynthesis
functional verification
Postsynthesis
timing verification
Test generation and
Fault simulation
Cell placement, scan chain and
clock tree insertion ,cell routing
Verify physical and Electrical design rules
Extract parasitic
Design sign-off
Production-ready masks
Chap1.4~1.6
Front-End
Back-End
FPGA
ASIC

## Slide 169: Hierarchy for IC design
n+
n+
S
G
D
DEVICE
CIRCUIT
GATE
MODULE
SYSTEM
+
Chap1.2
Chap1.3

## Slide 170: Hierarchy for IC design
n+
n+
S
G
D
DEVICE
CIRCUIT
GATE
MODULE
SYSTEM
+
Chap1.2
Chap1.3

## Slide 171: Hierarchy for IC design
n+
n+
S
G
D
DEVICE
CIRCUIT
GATE
MODULE
SYSTEM
+
Chap1.2
Chap1.3

## Slide 172: Hierarchy for IC design
n+
n+
S
G
D
DEVICE
CIRCUIT
GATE
MODULE
SYSTEM
+
Chap1.2
Chap1.3

## Slide 173: Hierarchy for IC design
n+
n+
S
G
D
DEVICE
CIRCUIT
GATE
MODULE
SYSTEM
+
Chap1.2
Chap1.3

## Slide 174: CPU Design & Implement

## Slide 175: CPU Design & Implement
an idea
(By Manual)

## Slide 176: CPU Design & Implement
A declarative statement or written expression to specifying the idea in text, diagram or HDL language (By Manual)
an idea
(By Manual)

## Slide 177: CPU Design & Implement
A declarative statement or written expression to specifying the idea in text, diagram or HDL language (By Manual)
an idea
(By Manual)
MIH R0 1
MIL R0 0
ADD R0 R1
SUB R0 R1
CMP R0 R1
MUL R0 R1
AND R0 R1
ORR R0 R1
NOT R0
SHL R0
SHR R0
JNZ 10
JPA 10
LDA R0 R1
STR R0 R1
INP R0 R1
OUP R0 R1
The ISA
for a CPU

## Slide 178: CPU Design & Implement
A declarative statement or written expression to specifying the idea in text, diagram or HDL language (By Manual)
an idea
(By Manual)

## Slide 179: CPU Design & Implement
A declarative statement or written expression to specifying the idea in text, diagram or HDL language benefits (By Manual)
Partitioning problem into functional blocks, balancing tradeoff between costs and benefits (By Manual)
an idea
(By Manual)

## Slide 180: RTL design for A Typical Digital circuit
2026-08-30
179
Data Inputs
Data Outputs
Control Signals
Status Signals
Control Inputs
Control Outputs
Controller
Datapath
Chap1.1

## Slide 181: RTL design for A Typical Digital circuit
2026-08-30
180
Data Inputs
Data Outputs
Control Signals
Status Signals
Control Inputs
Control Outputs
Controller
Datapath
Chap1.1

## Slide 182: RTL design for A Typical Digital circuit
2026-08-30
181
Data Inputs
Data Outputs
Control Signals
Status Signals
Control Inputs
Control Outputs
Controller
Datapath
Chap1.1

## Slide 183: RTL design for A Typical Digital circuit
2026-08-30
182
Register Transfer Level Design
Data Inputs
Data Outputs
Control Signals
Status Signals
Control Inputs
Control Outputs
Controller
Datapath
Chap1.1

## Slide 184: CPU Design & Implement
A declarative statement or written expression to specifying the idea in text, diagram or HDL language benefits (By Manual)
Partitioning problem into functional blocks, balancing tradeoff between costs and benefits (By Manual)
an idea
(By Manual)

## Slide 185: CPU Design & Implement
A declarative statement or written expression to specifying the idea in text, diagram or HDL language benefits (By Manual)
Partitioning problem into functional blocks, balancing tradeoff between costs and benefits (By Manual)
Register Transfer Level (RTL) (By Tools) Logic Level (Gate) (By EDA tools) Transistor level (By EDA tools)
an idea
(By Manual)

## Slide 186: An HDL file
P8
Verilog
P9
VHDL

## Slide 187: An HDL file
module adder8 (
input …… ,
output ……….
);
wire …… ;
always@(……)
begin
……………
end;
always@(……)
begin
……………
end;
endmodule
P8
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
USE IEEE.STD_LOGIC_UNSIGNED.ALL;
ENTITY adder8 IS
…………….
END adder8;
ARCHITECTURE one OF adder8 IS
SIGNAL ……;
BEGIN
PROCESS(……)
BEGIN
……………
END PROCESS;
PROCESS(……)
BEGIN
……………
END PROCESS;
END one;
Verilog
P9
VHDL

## Slide 188: An HDL file
module adder8 (
input …… ,
output ……….
);
wire …… ;
always@(……)
begin
……………
end;
always@(……)
begin
……………
end;
endmodule
P8
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
USE IEEE.STD_LOGIC_UNSIGNED.ALL;
ENTITY adder8 IS
…………….
END adder8;
ARCHITECTURE one OF adder8 IS
SIGNAL ……;
BEGIN
PROCESS(……)
BEGIN
……………
END PROCESS;
PROCESS(……)
BEGIN
……………
END PROCESS;
END one;
Verilog
P9
VHDL

## Slide 189: An HDL file
module adder8 (
input …… ,
output ……….
);
wire …… ;
always@(……)
begin
……………
end;
always@(……)
begin
……………
end;
endmodule
P8
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
USE IEEE.STD_LOGIC_UNSIGNED.ALL;
ENTITY adder8 IS
…………….
END adder8;
ARCHITECTURE one OF adder8 IS
SIGNAL ……;
BEGIN
PROCESS(……)
BEGIN
……………
END PROCESS;
PROCESS(……)
BEGIN
……………
END PROCESS;
END one;
Verilog
P9
VHDL

## Slide 190: An HDL file
module adder8 (
input …… ,
output ……….
);
wire …… ;
always@(……)
begin
……………
end;
always@(……)
begin
……………
end;
endmodule
P8
LIBRARY IEEE;
USE IEEE.STD_LOGIC_1164.ALL;
USE IEEE.STD_LOGIC_UNSIGNED.ALL;
ENTITY adder8 IS
…………….
END adder8;
ARCHITECTURE one OF adder8 IS
SIGNAL ……;
BEGIN
PROCESS(……)
BEGIN
……………
END PROCESS;
PROCESS(……)
BEGIN
……………
END PROCESS;
END one;
Verilog
P9
VHDL

## Slide 191: CPU Design & Implement
A declarative statement or written expression to specifying the idea in text, diagram or HDL language benefits (By Manual)
Partitioning problem into functional blocks, balancing tradeoff between costs and benefits (By Manual)
Register Transfer Level (RTL) (By Manual) Logic Level (Gate) (By EDA tools) Transistor level (By EDA tools)
an idea
(By Manual)

## Slide 192: CPU Design & Implement
A declarative statement or written expression to specifying the idea in text, diagram or HDL language benefits (By Manual)
Check whether implementation matches spec. in a Iterative process (By Manual and EDA tools )
Partitioning problem into functional blocks, balancing tradeoff between costs and benefits (By Manual)
Register Transfer Level (RTL) (By Manual) Logic Level (Gate) (By EDA tools) Transistor level (By EDA tools)
an idea
(By Manual)

## Slide 193
2026-08-30
    Test for a digital circuit
Simulation
Hardware
Verification
Final Prod.
test

## Slide 194: TestBench Anatomy
TestBench Module
Design Module
Stimulus Generater
Apply Inputs
Response Monitor
Observe Outputs
module My_tb; --TestBench module has no ports
    reg ……….; --Local signals and constants
    wire ……….;
Instantiating module; -- Instantiations of DUT
initial begin ……… end -- Input stimuli: reset
always begin ……… end -- Input stimuli: clock
initial begin ……… end -- Input stimuli: other signals
always @ ( posedge clock ) begin
……… -- Compare results
end
always @ ( posedge clock ) begin
……… -- Display results
end
endmodule
Design Under Test

## Slide 195: A Simple Tester
`timescale 1ns/100ps
module Detector110Tester;
reg aa, clock, rst;
wire ww;
Detector110 UUT (aa, clock, rst, ww);
initial begin
aa = 0; clock = 0; rst = 1;
end
initial repeat (44) #7 clock = ~clock;
initial repeat (15) #23 aa = ~aa;
initial begin
#31 rst = 1;
#23 rst = 0;
end
always @(ww) if (ww == 1)
$display ("A 1 was detected on w at time = %t", $time);
endmodule
No input or output ports
Inputs & Outputs of DUT
The Instantiation of DUT (Detector110 Module)
An initial statement
Generates a periodic signal :
repeats (44) times with (7time steps) delay,
Generates a no-periodic signal
A Verilog System Task: reports the Times at which the ww Variable becomes 1
Time unit

## Slide 196
2026-08-30
THE END OF TOPIC1
Digital Logic Design and Application
Topic 1 - Introduction Yan Bo
School of Information & Communication Engineering, UESTC
Email: yanboyu@uestc.edu.cn
195

## Slide 197: Homework 1
P59 2.1 （ e ）、2.2 （ e ）、2.3 （ f ）
2.6（ c ）、 2.8（ d ）
Additional question
=5
Decide the radix used from the equation:

## Slide 198
P17 1.9、1.10
P60 2.4（ b ）、 2.5（ c ）、2.7（ d ）、 2.10（ c ）
2.12（ c ）、2.14（ d ） 、2.27（a）（b）、
2.28（ C ）、 2.34、 2.35
P106 3.1 （ d ） 、3.2（ d ） 、3.4（a）,（e）
3.23（c）（f）、3.26 （a）、3.11、3.17（b）
3.36
P151 4.2、4.25 、4.28、4.32
Homework 2

## Slide 199: Homework 2（ Additional questions ）
2. Please finish the function as below:
1) Consider the 8-to-1 MUX as a single component shown here
2) Use 1 pcs 74LS138 to finish the same F(x,y,z), other basic gates are also allowed to be used.
F (x, y, z) = x'y'z' + x'yz' + xy'z + xyz' + xyz.
1. Using Karnaugh maps, find a minimal SOP expression and a minimal POS expression for each of the following logic functions. Indicate the distinguished 1-cells (or 0-cells) in each map.
(a) F= Sx,y,z(1,3,5,6,7)
(b) F= SW,X,Y ,Z(0,1,2,8,11)+ d(3,9,15)

## Slide 200: Homework 3
P211
5.1、5.3、5.4、5.8、5.10
P270
6.1（a）、 6.3（a）、6.4、6.7

## Slide 201
P111 3.30、3.31
P212 5.7
Homework 4

## Slide 202: Homework 5
A benchmark program runs on a 40MHz processor. The executed program consists of 100,000 instruction, with the following instruction mix and clock cycle count. Determine the effective CPI, MIPS rate and execution time T for this program.
Instruction type | Instruction count | Cycles per instruction
Integer arithmetic | 45000 | 1
Data transfer | 32000 | 2
Floating point | 15000 | 2
Control transfer | 8000 | 2