## Slide 1: Digital Logic Design and Application
Lab Course 2
Lecturer:
TA:
Lab Room:

## Slide 2: Requirements
1. Understand the working flow of CPU.
2. Consider about control signals needed in datapath module.
3. Finish the alu module based on the code given in txt.
4. Simulate and check the results.

## Slide 3: Content
EDA tools
Datapath Design
  Compose a specification for basic CPU: instruction set, etc;
  Design ALU component;
  Coding, Synthesis and simulate ALU component;
Controller Design
CPU Integration
CPU Design Improvement

## Slide 4: Process to execute program
Fetch
Analysis
Execute
AB
DB
ALU
R1
Temp
Status Register
Register
File
Operation Controller
Instruction Decoder
Instruction
opcode, oprand
Internal CPU BUS
Address Buffer
Data Buffer
Program
Counter
Decoder
Read
B0
5C
04
2E
Address
1001
1002
1003
Data
1000
Main memory
MOV 0x5C, R1
ADD R1, 0x2E, R1
＋1
Outside
Of CPU
Inside
of CPU
①
②
③
④
⑤
⑥
①
②
③
④
⑤
⑥
①
③
④
⑤
⑥
②
①
②
③
④
⑤
⑥
⑦
⑧

## Slide 5: CPU Organization
CPU
Control
Unit
Datapath
state_transition
Control Unit
ALU &
ALU MUX
Registers
Datapath
PC
IR

## Slide 6: Top structure of our CPU
Data
path
Control
Unit
Regs control signals
ALU control signals
CPU
Reg group
Alu
PC
Alu_mux
IR
State
transition
PC control signal
En_group, Reg_en
Opcode
Alu_in_sel Alu_in_sel
En_pc pc_ctrl
Other signals

## Slide 7: Instruction Set
Opcode | Rd | Rs | Imme | assembly | function
4bit | 2bit | 2bit | 8bit |  | 
0000 | 01 | xx | 00000010 | Mov R1 #02 | R1<= 2
0010 | 01 | xx | 00001000 | Add R1 #08 | R1<=(R1)+8
0101 | 01 | 10 | xxxxxxxx | Sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | And R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | Or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | Jump #01 | PC<= 1
Opcode supports 16 instructions. So you can add other instructions, like shift, multiplication.
Rd and Rs can be expressed in 2 bits that means you can operate 4 registers.
Immediate data is expressed in 8 bits.

## Slide 8: Instruction Set
Opcode | Rd | Rs | Imme | assembly | function
4bit | 2bit | 2bit | 8bit |  | 
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | Mov R1 #02 Mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | Add R1 #08 Add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | Sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | And R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | Or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | Jump #01 | PC<= 1
Opcode supports 16 instructions. So you can add other instructions, like shift, multiplication.
Rd and Rs can be expressed in 2 bits that means you can operate 4 registers.
Immediate data is expressed in 8 bits.

## Slide 9: Datapath Design
pc_ctrl | pc_out
00 | pc_out
01 | pc_out + 1
10 | offset_addr

## Slide 10: reg_group
rd/rs （read address） | rd_q/rs_q （read data）
00 | R0
01 | R1
02 | R2
03 | R3
reg_en （write address） | R0 | R1 | R2 | R3
0000 | R0 | R1 | R2 | R3
0001 | alu_out | R1 | R2 | R3
0010 | R0 | alu_out | R2 | R3
0100 | R0 | R1 | alu_out | R3
1000 | R0 | R1 | R2 | alu_out
others | error |  |  | 

## Slide 11: ALU MUX
always @( negedge rst or posedge clk )
begin
if(rst ==1'b0)
begin
alu_a <= xxx;
alu_b <= xxx;
en_out <= xxx;
end
else if(en_in == 1'b1)
begin
alu_a <= rd_q;
en_out <= 1'b1;
if(alu_in_sel ==1'b0)
alu_b <= xxx;
else
alu_b <= xxx; end
end
alu_in_sel | alu_a | alu_b
0 | Rd_q | offset
1 | Rd_q | Rs_q
alu_a can be get directly

## Slide 12: ALU
case ( alu_fuction )
XXX
endcase
alu_func | alu_out
000 | alu_b
001 | alu_a + alu_b
010 | alu_a - alu_b
011 | alu_a and alu_b
100 | alu_a or alu_b
The function of ALU is determined by the instructions we have set.

## Slide 13: 1. Create New Hardware Project
Follow the steps of lab1.ppt to create New Hardware Project

## Slide 14
2. Create New Source File -step1
Add files in the code folder as following steps.

## Slide 15
Click here
2. Create New Source File -step2

## Slide 16
2. Create New Source File -step3
Find the code folder, and choose *.v file
Click here

## Slide 17
2. Create New Source File -step4
Complete the ALU module.

## Slide 18
3. Do Synthesis and get the circuit
Follow the steps of lab1.ppt to do Synthesis and get the circuit

## Slide 19
4. Create Simulation Source
File -step1
Copy the content in tb_alu.txt to this window, and complete the code

## Slide 20
4. Create Simulation Source
File
-step2
1.Right- click
2.Click

## Slide 21
4. Create Simulation Source
File
-step3
Observe the variation of signals. Make sure all of these are right.

## Slide 22: How to make a testbench
1、All the input should be given.
2、You need a clock, and how to create it?
3、With the time going, you can change your input.
4、Complete the testbench on the next page.

## Slide 23: How to make a testbench
parameter Tclk = 10;
initial begin
clk=0;
forever #(Tclk/2) clk=~clk;
end
initial begin
rst=0;
#(Tclk*4) rst=1;
end
initial begin
alu_func = 3'b000 ;
#(Tclk*8) alu_func = 3'b001 ;
//please add rest code here
end
initial begin
alu_a = 16'b0000000100000001;
alu_b = 16'b0000000000010001;
end
reg cnt1;
always @ (posedge clk) begin
if(!rst)
cnt1 <= 1'd0;
else
cnt1 <= cnt1+1;
end
always @ (posedge clk) begin
if(!rst)
en_in <= 1'b0;
else if (cnt1==1'd1)
en_in <= 1'b1;
else
en_in <= 1'b0;
end
initial begin
#(Tclk*40) $stop;
end
endmodule
module tb_alu();
reg clk,rst,en_in;
reg [15:0] alu_a;
reg [15:0] alu_b;
reg [2:0] alu_func;
wire en_out;
wire [15:0] alu_out;
alu test_alu(
.clk (clk),
.rst (rst),
.en_in (en_in),
.alu_a (alu_a),
.alu_b (alu_b),
.alu_func (alu_func),
.en_out (en_out),
.alu_out (alu_out)
);

## Slide 24: RTL of Datapath

## Slide 25: Digital Logic Design and Application
Lab Course 2
~~End~~