## Slide 1: Digital Logic Design and Application
Lab Course 3
Lecturer:
TA:
Lab Room:

## Slide 2: Requirements
1. Understand the function of the control unit in CPU.
2. Consider about the controller’s STG according to the ISA.
3. Finish the state_transition module based on the given codes .
4. Simulate and check the results.

## Slide 3: Content
EDA tools
Datapath Design
Controller Design
  Understand the STG for control_unit ;
  Design state_transition component;
  Coding, Synthesis and simulate state_transition component;
CPU Integration
CPU Verification and Improvement

## Slide 4: CPU Organization
CPU
Control
Unit
Datapath
state_
transition
Control Unit
ALU &
ALU MUX
Registers
Datapath
PC
IR

## Slide 5: Top structure of our CPU
Data
path
Control
Unit
Regs control signals
ALU control signals
CPU
Reg group
Alu
PC
Alu_mux
IR
State
transition
PC control signal
En_group, Reg_en
Opcode
Alu_in_sel Alu_in_sel
En_pc pc_ctrl
Other signals

## Slide 6: Instruction Set
Opcode | Rd | Rs | Imme | assembly | function
4bit | 2bit | 2bit | 8bit |  | 
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | Mov R1 #02 Mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | Add R1 #08 Add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | Sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | And R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | Or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | Jump #01 | PC<= 1
Opcode supports 16 instructions. So you can add other instructions, like shift, multiplication.
Rd and Rs can be expressed in 2 bits that means you can operate 4 registers.
Immediate data is expressed in 8 bits.

## Slide 7: State transition

## Slide 8: Control signals & state signal meaning
Control signals
Reg_group
en_group: enable signal, whether get datas from register group
reg_en: enable signal, means whether enable 4 registers to store datas to registers
Alu_mux
alu_in_sel: think about in the previous class
Alu
alu_in_func: think about in the previous class
PC
en_pc: enable signal, whether enable pc unite
pc_ctrl: mux signal, if pc_ctrl = 00 means pc_out <= pc_out ;
if pc_ctrl = 01 means pc_out <= pc_out +1;
if pc_ctrl = 10 means pc_out <= offset;
State signal
en_alu: enable signal, whether the datapath is completed

## Slide 9
Controller Design

## Slide 10: 1. Create New Hardware Project
Follow the steps of lab1.ppt to create New Hardware Project

## Slide 11
2. Create New Source File -step1
Add files in the code folder as following steps.

## Slide 12
Click here
2. Create New Source File -step2

## Slide 13
2. Create New Source File -step3
Refer to the next page to complete the state_transition module.

## Slide 14
en_in
en1
en2
2. Create New Source File -step4

## Slide 15
3. Do Synthesis and get the circuit
Follow the steps of lab1.ppt to do Synthesis and get the circuit

## Slide 16
Copy the content in tb_state_transition.txt to this window, and complete the code
4. Create Simulation Source
File -step1

## Slide 17
4. Create Simulation Source
File
-step2
1.Right- click
2.Click

## Slide 18
4. Create Simulation Source
File
-step3
Run simulation and observe the variation of signals. Make sure all of these are right.

## Slide 19: Digital Logic Design and Application
Lab Course 3
~~End~~