## Slide 1: Digital Logic Design and Application
Lab Course 4
Lecturer:
TA:
Lab Room:

## Slide 2: Content
EDA tools ( testbench)
Datapath Design
Controller Design
CPU Integration
  Combine the datapath and the controller;
  Synthesis;
  Compose the testbench and do simulation.
  CPU Verification and Improvement

## Slide 3: CPU Organization
CPU
Control
Unit
Datapath
state_transition
Control Unit
ALU
Registers
Datapath
PC
IR

## Slide 4: Top structure of our CPU
Data
path
Control
Unit
Regs control signals
ALU control signals
CPU
Reg group
Alu
PC
Alu_mux
IR
State
transition
PC control signal
En_group, Reg_en
Opcode
Alu_in_sel Alu_in_sel
En_pc pc_ctrl
Other signals
module cpu(....);
input XXXX
output XXXX
wire XXXX
reg XXXX
data_path data_path1 (XXXX);
control_unit1(XXXX);
endmodule

## Slide 5: Instruction Set
Opcode | Rd | Rs | Imme | assembly | function
4bit | 2bit | 2bit | 8bit |  | 
0000 | 01 | xx | 00000010 | Mov R1 #02 | R1<= 2
0010 | 01 | xx | 00001000 | Add R1 #08 | R1<=(R1)+8
0101 | 01 | 10 | xxxxxxxx | Sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | And R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | Or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | Jump #01 | PC<= 1
Opcode supports 16 instructions. So you can add other instructions, like shift, multiplication.
Rd and Rs can be expressed in 2 bits that means you can operate 4 registers.
Immediate data is expressed in 8 bits.

## Slide 6: Block design for Datapath

## Slide 7: Block design for Control_unit

## Slide 8: 1. Create New Hardware Project
Follow the steps of lab1.ppt to create New Hardware Project

## Slide 9
2. Create New Source File -step1
Follow the steps of lab2.ppt to add files in the code folder

## Slide 10
2. Create New Source File -step2
Refer to the next page to combine data_path and control_unit in cpu.v

## Slide 11
2. Create New Source File -step3

## Slide 12
3. Do Synthesis and get the circuit
Follow the steps of lab1.ppt to do Synthesis and get the circuit

## Slide 13
Copy the content in tb_cpu.txt to this window, and complete the code.
You can refer to previous test bench.
4. Create Simulation Source
File -step1

## Slide 14
4. Create Simulation Source
File
-step2
Run simulation and observe the variation of signals. Make sure all of these are right.

## Slide 15: Some other ideas for Instruction Set
Memory access instructions
Ldr, Str
Conditional branch instructions
Jz, Jnc, …
Other data operation instructions
  Xor, Cmp…..
  Acc (add 1 to N)

## Slide 16
Improve your testbench
Design a benchmark (program for test)
Design a memory BFM
(Behavior Function Module)
Figure out some timing issues

## Slide 17: Digital Logic Design and Application
Lab Course 4
~~End~~